## Slide 1: HiPERCOM Standardization Activities at the IETF
Emmanuel Baccelli

## Slide 2: IP: From Wired to Wireless…
Cellular
IP Link
Wired
IP Link
INTERNET
Router
User terminals
User terminals
INTERNET
Router

## Slide 3: … Towards Wireless Prosumers
Cellular
wireless
networks
Spontaneous
wireless
networks
Router
User terminals
(Consumers)
(Producers)
(Prosumers)

## Slide 4: Spontaneous Wireless Networking
Self-organized wireless networking, multi-hop, with or without help from infrastructure.
Ad hoc networks
Wireless Mesh networks
Sensor/actuator networks
Opportunistic networks
Vehicular Networks
…

## Slide 5: IP & Spontaneous Wireless Networks
Most protocols in the IPv4 or IPv6 suite designed w.r.t. some assumptions
      High-Definition IP links
      End-to-end connectivity exists
      Routers are always on, if not dead
      Routers have reasonable memory, CPU, power
      Frame sizes are not unreasonably small
Most spontaneous wireless networks break these assumptions => need for new standards

## Slide 6: The IETF
IETF = Internet Engineering Task Force
Standardization
  New domains
  Compatibility
Maintenance
  Legacy
  Compatibility
Internet Protocols
Users
Multiple vendors

## Slide 7: IETF Standards?
Specifications in documents called Request For Comments: RFC
  for instance TCP was first specified in RFC 793
Before becoming an RFC, a specification must mature as an Internet Draft
  Not all drafts become an RFC
  Multiple draft stages until RFC status
  RFC completion-time unit = year(s)

## Slide 8: RFC authors over the Years

## Slide 9: What makes a good standard?
A ‘good idea’ is not always a good idea (i.e. compatibility with legacy)
Be conservative in what you do, liberal in what you accept from others (J. Postel principle)
Robustness even in extreme case (eg TCP)

## Slide 10: Recent HiPERCOM RFCs
RFC 5148 "Jitter considerations in MANETs", February 2008. Clausen T., Dearlove C. and Adamson B.
RFC 5444 "Generalized MANET Packet/Message Format", February 2009. Clausen T., Dearlove C., Dean J., and Adjih C.
RFC 5449 "OSPF Multipoint Relay (MPR) Extension for Ad Hoc Networks" , February 2009. Baccelli E., Clausen T., Nguyen D., and Jacquet P.
RFC 5497 “Representing Multi-Value Time in MANETs”, March 2009 Clausen T., Dearlove C.
RFC 5889 “IP Addressing Model in Ad Hoc Networks”, September 2010. Baccelli E. and Townsley M.
RFC 6130 "Mobile Ad Hoc Network (MANET) Neighborhood Discovery Protocol", April 2011. Clausen T., Dean J., and Dearlove C.
RFC 6206 "The Trickle Algorithm", March 2011. Levis P., Clausen T., Hui J., Gnawali O, and Ko J.

## Slide 11: Mature HiPERCOM Internet Drafts
P2P-RPL draft “Reactive Discovery of Point-to-Point Routes in Low Power and Lossy Networks”, Baccelli E., Goyal M. et al. Last call in March 2012.
P2P-MEASUREMENT draft “A Mechanism to Measure the Quality of a Point-to-point Route in a Low Power and Lossy Networks”, Baccelli E., Goyal M. et al. Last call in March 2012.
PACKETBB-SEC draft “Integrity Check Value and Timestamp TLV Definitions for MANETs”, Clausen T., and Herberg. U. Last call March 2012.
OLSRv2 draft "The Optimized Link State Routing Protocol version 2", Internet-Draft, March 2012 Clausen T., Dearlove C., and Jacquet, P.
NHDP-SEC-THREATS draft "Security Threats for NHDP", Internet-Draft, March 2012. Clausen T., Yi J, and Herberg U.
NHDP-SEC draft "Using Integrity Check Values and Timestamps in NHDP", Internet-Draft, March 2012. Clausen T., and Herberg U.
NHDP-MIB draft "Definition of Managed Objects for NHDP", Internet-Draft, September 2011 Herberg U., Cole R., Chakeres I.

## Slide 12: New HiPERCOM Internet Drafts
RPL-EXP draft “Experiences with RPL: IPv6 Routing Protocol for Low power and Lossy Networks”, Internet-Draft, March 2012. T.Clausen, J,Yi, A. Colin de Verdiere, U. Herberg.
WIRELESS-COMM draft “Multi-hop Ad Hoc Wireless Communication”, Internet Draft, 2011. E. Baccelli, C. Perkins.
LOADng draft “The LLN On-demand Distance-vector Routing Protocol - Next Generation(LOADng)” Internet-Draft, March 2012. T.Clausen, A.Colin de Verdiere, J.Yi, Y.Igarashi, H.Satoh.
RPL-DIS draft “DIS Modifications”, Internet Draft, 2012. E. Baccelli, M. Goyal, D. Barthel, N. Dejean, J. Martocci.

## Slide 13: Agenda
Wireless ad hoc & mesh networks
Internet of things & sensor networks

## Slide 14: IP Links: the atoms of the Internet
IP links were modeled after Ethernet:
At time T, through interface i on the IP link:
U = set of devices that hear node X
V = set of devices that node X hears
Symmetry: U=V
Stability: U, V sets usually same at time T+1
Transitivity: if the pairs (A,B) and (A,C) can hear each other, then the pair (B,C) can hear each other
R
User terminals
A
i
B
C
D
=> High-Definition links with predetermined properties

## Slide 15: Wireless Ad Hoc & Mesh Networks
DISRUPTION: links are no longer well defined and are unstable in general
A
B
C
D
At time T, through interface i :
U = set of devices that hear node X
V = set of devices that node X hears
Assymetry: U≠V
Time-variation: U, V sets usually ≠ at T+1
Non-transitivity: pairs (A,B) and (B,C) hearing each other means nothing about how (A,C) can communicate
=> Low-Definition links with undetermined connectivity
E. Baccelli, C. Perkins ‘Multi-hop Ad Hoc Wireless Communication’, IETF Internet Draft, 2011.

## Slide 16: Routing in Ad Hoc and Mesh Networks
More dynamic links, less bandwidth (wireless)
Traditional routing protocols (eg OSPF) fail
New routing schemes are needed (eg OLSR)
wireless routers

## Slide 17: OSPF extension for Hybrid Networks
How to efficiently route in hybrid networks?
Combining OLSR agility with OSPF compatibility
Standard: RFC 5449
wired routers
wireless routers
E. Baccelli, T. Clausen, P. Jacquet,
D. Ngyuen ‘MPR-OSPF’, IETF RFC 5449, 2009.

## Slide 18: Autoconfiguration in Ad Hoc & Mesh Networks
Prior to routing, devices need appropriate IPv4/v6 configuration
      eg. IP address, prefix etc.
Standard autoconfiguration protocols (ND, SLAAC, DHCP) fail on low-def. links
What is the appropriate configuration of an interface on a low-def link?
IPv6 Standard: RFC 5889
E. Baccelli, M. Townsley, ‘IP Addressing Model in Ad Hoc Networks’, IETF RFC 5889, 2010.
E. Baccelli, K. Mase et al, ‘Address Autoconfiguration for MANET: Terminology and Problem Statement’, IETF Internet Draft, 2008.
186.12.134.1
186.12.12.13
186.12.2.115
186.12.19.5
186.12.77.16
186.12. 38.9
186.12.1.1

## Slide 19: Agenda
Wireless ad hoc & mesh networks
Internet of things & sensor networks

## Slide 20: Internet of Things
A buzz word for the upcoming avalanche of connected devices other than terminals/routers
INTERNET
Sensors
Smartphone Sensors
Home Appliances
Smart Dust
Cars Floating Data

## Slide 21: Sensor Networks
DISRUPTION: same as ad hoc networks, plus stringent CPU, memory, frame-size and power management constraints.
Typically 8-16 bits micro-controllers, a few kB of RAM, a few 10kB of ROM, slightly less than the first computers on the ARPANET!
Agressive sleep modes, duty cycles
IEEE 802.15.4 payload is 81 octets(IPv6 MTU is 1280 octets)
Even MANET protocols don’t fit as-is!!

## Slide 22: Routing in Sensor Networks
Assumptions on data traffic and mobility patterns led to tree-based IPv6 routing standard-to-be RPL
R
S
D
R
S
D
DAG
Path with basic RPL
Several limitations, especially in Home/Building Automation
Longer paths
Congestion near root
T.Clausen, J,Yi, A. Colin de Verdiere, U. Herberg.
“Experiences with RPL: IPv6 Routing Protocol for Low power and Lossy Networks”, Internet-Draft, March 2012.

## Slide 23: Routing in Sensor Networks
P2P-RPL: extension for on-demand efficient sensor-to-sensor routing
R
S
D
R
S
D
Path with basic RPL
Path with P2P extension
Based on reactive tech.
Path request dissem.
Path reply unicast
M. Goyal, E. Baccelli, et al., ‘Reactive Discovery of Point-to-Point Routes in Low Power and Lossy Networks’, IETF Internet Draft, 2012.

## Slide 24: P2P-RPL Implementation & Experiments
  Significant path length reduction
  Significant traffic reduction near root
Senslab testbed in Lille
(MSP430-based, 802.15.4 at 2,4GHz)

## Slide 25: Conclusion & Perspectives
Many novel/updated IPv6/v4 protocols needed
      Standard DTN routing
      Standard IP autoconfiguration on MANET
      Standard sensor network routing
      …
Design & Standardize
Analyze & Model
Implement,
Simulate
& Experiment
These new standards should be optimized through virtous cycles such as: