## Slide 1: Application Level- FEC @ Planète
Vincent Roca
March 23rd, 2012

## Slide 2: Context
AL-FEC codes are
  codes for the erasure channel
  working in “upper layers”
    application, transport, or MAC
  they are easily implemented in a software codec
good AL-FEC codes have
    high erasure recovery capabilities
    low encoding and/or decoding complexity
  an AL-FEC solution is often the result of trade-offs
working both on codes and codecs is required

## Slide 3: The big picture
AL-FEC
(codes, codecs,
perf. evaluation framework)
Application to use-cases
(AL-FEC schemes,
filecasting and robust streaming,
UEP, file bundle protection)
IETF standardization
(RFC 5170, 5510, 6363
+ 4 I-D on the subject)
LDPC-Staircase@ISDB-Tmm
(push VOD service to mobiles)
http://openfec.org
(“because open, free AL-FEC
codes and codecs matter”)
commercial LDPC-Staircase
codec (Expway)
2nd generation LDPC codes
(the successor…)
1st generation codes
(LDPC-Staircase)


## Slide 4: Motivations for a 2nd generation
LDPC-Staircase codes are already a good and practical solution
    in spite of their simplicity
…but let’s see if we can go further
« Analysis of Quasi-Cyclic LDPC codes under ML decoding over the erasure channel »
    Mathieu Cunche*, Valentin Savin+, Vincent Roca*
    *Inria, +CEA-LETI
    IEEE Int. Symposium on Information Theory and Applications (ISITA’10), October 2010.

## Slide 5: Quick introduction to LDPC
binary “Low Density Parity-Check”
  characterized by a sparse parity-check matrix
X1  X4  X5  X7  X8  X10 = 0
Source + repair symbols
Constraints
0
1
1
1
0
1
0
1
1
0
1
0
0
1
1
0
1
1
0
1
1
1
1
0
0
0
1
1
0
1
0
0
1
1
1
1
1
0
1
0
1
1
0
0
1
1
0
0
1
1
X1
X2
X3
X4
X5
X7
X8
X9
X10
X6
H X = 0
Notes: LDPC Gallager 1963
Chaque équation définit une contrainte
Cas binaire: somme Xor

## Slide 6: Quick introduction to LDPC… (cont’)
decoding consists in solving a linear system
two possible approaches
  iterative decoding (IT)
    linear complexity O(k) 
    sub-optimal erasure recovery capabilities 
  Maximum Likelihood decoding (ML)
    e.g. Gaussian elimination
    optimal erasure recovery capabilities 
    increased complexity O(k2) 
A Xe = B
HX= 0
He Xe = Hr Xr
erased symbols
received symbols

## Slide 7: Quick introduction to LDPC… (cont’)
our goals
  reduce ML decoding complexity
  while keeping the same erasure recovery capabilities for ML and IT
our proposal
  use structured codes
  take advantage of a known result:
  Gaussian elimination complexity is
  reduce to O(kB) row operations if
  the system has a band of width B
B
0
0
k

## Slide 8: Quasi-Cyclic LDPC codes
definition
  create a base matrix, generated according to specific rules, but with random non-binary values
  expend it Z times
bi,j
z
z
bi,j
b0,0
ba,0
ba,b
b0,b
…
…
…
…
mB
nB
mB*z
nB*z
1
1
1
1
1
1
1
1
base matrix
bloc-circulant
parity check
matrix
circulant identity
z*z matrix

## Slide 9: Quasi-Cyclic LDPC codes… (cont’)
a hidden “pseudo-band” structure can be exhibited
  simple row and column permutations
  the band width can be controlled via M
  reduces the ML decoding complexity
    complexity = O(kq)
band width is q = (M+1) nB
where M = max{bi,j}

## Slide 10: Quasi-Cyclic LDPC codes… (cont’)
what band width should we use?
  3 cases considered (k is an input parameter)
    q = cst theoretical ML complexity = O(k)
    q = O(√k) theoretical ML complexity = O(k √k)
    q = O(k) theoretical ML complexity = O(k2)
band width is q = (M+1) nB
where M = max{bi,j}

## Slide 11: Experimental results for ML decoding
    inefficiency ratio =
    choosing q = √k does not reduce average erasure recovery performance WRT q = k under ML decoding
nb symbols required to decode
k
Code dimension (k)
Average Inefficiency Ratio
q = cst
q = O(√k)
q = O(k)

## Slide 12: Experimental results for ML decoding…
    choosing q = √k significantly reduces complexity WRT q = k under ML decoding
Code dimension (k)
Average number of symbol operations
q = cst
q = O(√k)
q = O(k)

## Slide 13: Conclusions
using q = O(√k) is appropriate
    exhibits good results
    simple design
further optimizations are possible
    it is known that IT decoding is limited by the presence of “small cycles” in the parity check matrix
    by optimizing cycles in the base matrix we control cycles in the expanded parity check matrix