## Slide 1: Privacy & Security PLANETE GROUP
C. Castelluccia
INRIA

## Slide 2: Overview
Embedded
Systems
Security&Privacy
Internet/Network
Privacy
Code injection in
harvard-architecture
[CCS]
Security/Safety tradeoff
In critical systems
–IMD [CCS]
Privacy & Service Personalization (Google, Ads,…) [PETS]
Privacy in P2P architecture
(Skype, BT,…) [IMC,LEET]
Code attestation in
Embedded systems
[CCS;Esorics;NDSS]
Ephemeral Communications [ICNP]
Privacy-Preserving Smart Metering [IH;WPES]
Secure Aggregation[ToSN]
Adaptive Password Checking [NDSS]
Signal-Based
Security [PIMRC]
Notes: With UCI and Berkeley…

## Slide 3: Proximity-Based Access Control for IMD (Implantable Medical Devices)
ACM CCS’09

## Slide 4: Implantable Medical Devices
More and more IMD use wireless com.
  Ease configuration
  Allow to store and download data remotely(measures)
  Remote monitoring of patients

## Slide 5: Pacemakers/defibrillators
Current systems
  Ultra-low-power CPU + 128 ko. RAM (data patient, log,…)
  Communication by induction
  Short range
    Contact with patient
  Limited Bandwidth
New systems
  Longer range (~2m)
    Remote monitoring of patients
    Ease configuration and installation
  More Bw (~400 kbits/s)
    Enable new applications
    Reduction consultation time
Notes: 5

## Slide 6: IMD: The future!
Notes: 6

## Slide 7: Existing Attacks
[1] Halperin and al., Pacemakers and implantable cardiac defibrillators: Software radio attacks amd zero-power defenses, IEEE Security and Privacy, Oakland, 2008.

## Slide 10: Why this lack of Security?
Costly in term of ressource
  CPU, bandwidth, and battery!
  Reduce IMD lifetime
Safety/Security trade-off!
  Security should not jeopardize patient’s life i.e.
    We must stop attackers
    But authorize access in case of emergency!
  How to make the difference?
Notes: 10

## Slide 11: Pacemakers Security/ A challenging problem…
Reader authentication
  Token based approach:
    Pacemaker is configured with a key/token…that is given to the patient’s doctor…
      But what if the patient is travelling or need to go to emergency?
    Smart card?
      What if the patient was swimming and got in an avalanche…
  Certificate based approach:
    How to revoke malicious/compromized readers?
    How to set-up the PKI?
Notes: 11
Merger avec precedent…

## Slide 12: Our Scheme
Current schemes are « secure » because of induction communication
  Attackers has to be physically close…
Our idea:
  Emulate « communication induction » on wireless com. by using distance bounding techniques
  Secure: An reader is authorized to communicate with a pacemaker only if it is « close enough »
    Prevent remote attacks
  Flexible: Authorization distances are configurable
    Sensitive operations, such as configuration, 2-3 cm…
    Less sensitive operations, such as reading data, 1-2-3 meters.
Notes: 12

## Slide 21: Conclusion Properties of our Scheme
Notes: 21

## Slide 22: THANKS!

## Slide 23
Media Attention